Procedure to scale an analog input channel using the W_INT_REAL and SCALING function block in Concept

We have an analog input channel referenced at 300001.  The raw value of that channel is 0 to 32000 and we need to scale it to 0 and 100.

- Create 3 variables

- Click on the Set button and enter the following scaling parameters

- in_min : Lower limit of input scale

- in_max : Upper limit of input scale

- out_min : Lower limit of output scale

- out_max : Upper limit of output scale

- clip : ‘1” the output OUT is limited between out_min and out_max

- Insert the W_INT_REAL and the SCALING function block from the library.  Click on FFB sorted.

- Select the W_INT_REAL and SCALING Function blocks from the list

- Program these blocks as follow

- The input of the W_INT_REAL block is the raw value of the analog input channel to be scaled.

(0 to 32000)

- The PARA input on the SCALING block contains all the scaling parameters

- The Output of the scaling block is the scaled analog input. (0 to 100)